## Slide 1
Quiz 3 – November 2 2017
Question 1
The viscosity of shear thinning materials is independent of the shear rate
True
B. False

## Slide 2
Question 2 Select the right statement
The viscosity of time dependent fluids decreases with time because their structure are broken down by shear
The viscosity of shear thickening fluids decrease with shear rate
The viscosity of rheopectic fluids decreases with time
The viscosity of thixotropic shear thinning fluids decreases with shear rate
A & D

## Slide 3
Question 3 Select the right statement below (in blue)
Hint: A plate/orifice system is commonly used to measure the flowrate of a fluid in a pipe. The measurement consists in evaluating the pressure drop across the plate/orifice system, which is proportional to the flow rate.
Both shear thinning and Newtonian fluids can be measured without problem by the plate and orifice system
The plate and orifice system is more suitable for Newtonian fluids
The plate and orifice system is more suitable for shear thinning fluids
The plate and orifice system is no suitable for Newtonian and shear thinning fluids

## Slide 4
Question 4
Select the right statement related to pressure loss of a fluid circulating in a circular pipe
The pressure loss is independent of the material rheology
The pressure loss is independent of the pipe diameter
The pressure loss is a function of the fluid rheology but independent
on the pipe diameter
D. The pressure loss is a function of the fluid rheology and the pipe diameter 
E. The pressure loss is independent of the flowrate

## Slide 5
Question 5
The consistency index k of the power law model changes significantly with the temperature whereas the flow index n is practically independent of the temperature
True 
False